Management frame, Control frames, Data frames

---
Contents
- Management Frames
- Control Frames
- Data Frames

---
Management frames
- Management frames allow wireless devices to form a network and manage the connections.
- 12 management frames
  - Beacon frame- 1000
  - Probe request frame- 0100
  - Probe response frame-0101
  - Authentication frame- 1011
  - Association request frame- 0000
  - Association response frame- 0001
  - Reassociation request- 0010
  - Reassociation response- 001
  - Disassociation-1010
  - Deauthentication-1100
  - ATIM- 1001
  - Action- 1101

---
Management frame format

---
Beacon Frame
- Beacon frames are used by access points to communicate throughout the serviced area the characteristics of the connection offered to the cell members.
- Beacon frames are sent periodically, at a time called target beacon transmission time(TBTT).
- The beacon time interval is 100TU

---
Beacon frame format

---
Capability information field

---
Beacon frame capture

---
Probe Request frame
- Probe request is management frame which aimed at asking what network is available on this channel.
- The probe requests are usually sent to the broadcast DA address(ff:ff:ff:ff:ff:ff)
- Once the probe is sent, the emitting starts a ProbeTimer countdown and waits for answers.
- This Probe time is decided by vendor, but it is usually a lot shorter than a beacon interval.
- At the end of the timer, the station processes the answers it has received.
- If no answer was received,the station moves to the next channel and repeats the discovery process.
- The purpose of a probe request is typically to discover APS and their supported networks.

---
Probe response
- Upon receiving a probe request frame, a station in an IBSS or an AP will respond with a probe response frame.
- The probe response is sent as a unicast frame.
- The probe response is sent at the lowest common rate supported by both the station sending the probe request and the answering AP
- The probe response should be acknowledged by the receiving station,just like any other unicast frame.

---
Authentication frame
- The station sends the authentication frame to the AP to validate the device type means verify that the requesting station has proper 802.11 capabilities or not.
- Two types of authentication
  - Open system
  - Shared key exchange

---
Association request frame
- The Association frame is sent by the station to the Ap.
- The purpose of this exchange is for the station to join the cell and obtaina cell member identifier called an association ID

---
Association Response frame
- After acknowledging the request frame, the AP examines each field of the request and verifies whether they all matches its own 802.11 parameters.
- Once the station receives its association ID, it is associated to the cell and can start to communicate, sending data or moving to a second layer of authentication.
- If the association fails, the station receives in the status code the reason for the failure.

---
Deauthentication frame
- The station or AP can also send a deaunthentication frame.
- This frame is used when all communications are terminated

---
Disassociation Frame
- Once a station is associated to an AP, either side can terminate the association at any time by sending a diassociation frame.
- The disassociation frame may be the unicast or a broadcast

---
Reassociation Request Frame
- Reassociation request frame can be sent only by a station to an access point.
- The reassociation request frame is unicast and acknowledged frame.

---
Reassociation response frame
An AP uses the reassociation response frame in response to reassociation request frame.

---
ATIM Frame
- The ATIM frame is specific to IBSS networks and used for distribution of buffered frames to stations in sleep mode in the ad hoc network.
- Beacons in IBSS are sent by any participating stations.
- There is an ATIM window in the beacon to indicate that participating stations should not fall back to doze mode.
- During the ATIM window, the ATIM frame is used to distribute broadcast and multicast packets.

---
Action Frame
Action frames are used to trigger specific actions.

---
- Action frames allow a form of added control to the cell, where the station can tell the AP, or AP can tell one or several stations, “i need you to do this or that” or “This is what is going to happen.”
- Types of action frames:
  0-Spectrum management.
  1-Qos.
  2-DLS.
  3-Block Ack.
  4-Public.
  5-Radio measurement.
  6-Fast BSS transition.
  7-reserved
  8-SA query.
  9-Protected dual of public action.
  10-125 – reserved.
  126 - vendor-specific protected.
  127 – vendor specific.
  128-255 -Error.

---
Control frames
- Control frames assist with the delivery of the data and management frames.
- Control frames do not have frame body.
- Control frames contain only a layer 2 header and trailer.
- Transmitted at different data rates.

---
RTS/CTS Frames
- Request to send(RTS) and Clear to Send(CTS) frames are used to enhance the virtual carrier sense process.
- Request to send/clear to send is a mechanism that performs a NAV distribution and helps prevent collisions from occuring.
- The NAV distribution reserves the medium prior to the transmission of the data frame.
- When RTS/CTS is enabled on a station, every time the station wants to transmit a frame, it must perform an RTS/CTS is exchange prior to the normal data transmission.
- When the transmitting station begins to transmit data, it first sends a 20 octet RTS control frame.
- The duration value of the RTS frame includes the time needed for the subsequent frames in the transmit operation to be transmitted.

---
- After the RTS frame transmitted, the receiving station respond by sending 14-octet CTS control frame.
- The duration value of the frame includes the time needed for the subsequent frames in the transmit operation to be transmitted.

---
Acknowledgement Frame
Every time an 802.11 radio transmits a unicast frame, if the frame is received properly, the 802.11 radio that received the frame will reply with a 14 octet acknowledgement(ACK) frame

---
Block acknowledgement request

---
- A block acknowledgement improves channel efficiency by aggregating several acknowledgement into one single acknowledgement frame.
- When a station intends to use the Block ACK mechanism to transmit QoS data, it first checks to see whether the peer station is capable of performing the Block ACK mechanism.
- Each of the frames has the Ack Policy subfield in the QoS Control field set to Block ACK.

---
Block Acknowledgement
The Block Ack is used to acknowledge a block of QoS data frames, instead of acknowledging each unicast frame independently.

---
PS-Poll
- When a client statio is set for Power Save mode, it will shut down some of the trasceiver components for a period of time to conserve power.
- The station indicates that it is using Power save mode by changing the value of the Power Management bit set to 1, the access point is informed that the client station is using power management, and the access point buffers all of the client's 802.11 frames.
- If the access point is buffering a data for a station in power save mode, when the access point transmits its next beacon, the AID of the station will be seen in a field of the beacon frame known as the traffic indication map(TIM).

---
- The TIM field is a list of all stations that have undelivered data buffered on the access point waiting to be delivered.
- Every beacon will include the AID of the station until the data is delivered.
- After a sleep for longer period the station will be awaken and start to receive the beacon frames.
- When station receives a beacon, it checks to see whether its AID is set in the TIM, indicating that a buffered unicast frame waits.
- If so, the station will remain awake and send a 20-octect PS-Poll frame to the access point.
- After receiving the PS-Poll frame the ap will send the buffered unicast frame to the station.

---
Control Wrapper
- The Control Wrapper was defined by the 802.11n amendment, which defined high throughput(HT) transmissions.
- The control Wrapper used to carry any other control frame together with an additional HT Control field.
- The FCS files of the Control Wrapper frame is a typical FCS field containing a 32 bit CRC , calculated over all the fields of the MAC header and the frame body, in this case the Carried Frame field.

---
Contention free
- Two addition control frames
  - CF-End
  - CF-End+CF-ACK
- CF-End is a 20 octet frame that is used to indicate the end of a contention-free period
- The CF-End+CF-ACK frame, is a 20-octect frame that is used to indicate the end of a contention free period and acknowledge receipt of a frame.
- Both of these control frames defined for use with an optional medium access method known as Point Coordination function(PCF).

---
The Hidden Node problem

---
Data Frames
- Data frames transport the information across the network in the wireless portion of the user network.
- Each data frame is represented by a Type value of 10 and different group of 4 Subtype bits.

---
Subtypes
1. Null(no data):-Send by station
2. CF-Ack(no data):- Send by the station
3. CF- Poll(no data):- Send by the access point
4. CF-Ack+CF-Poll(no data):- Send by the Access point
5. Data :- Send by the station/Ap
6. Data+CF-Ack:- send by station
7. Data+CF-Poll:- Send by AP
8. Data+CF-Ack+CF-Poll:- send by AP
9. QoS data :- Send by the AP/station
10. QoS data+ CF-Ack :- Send by station
11. QoS Data+CF-Poll :- Send by AP
12. QoS Data+CF-Ack+CF-Poll :- Send by AP

---
Simple data frames

---
QoS and Non-Qos Data Frames

---
Thank you