What is the difference between the hub,bridge,switch,router?

Hub

1) Hub supports the layer1 in the OSI Model .
2) A hub, also called a network hub, is a common connection point for devices in a network.
3) Hubs are devices commonly used to connect segments of a LAN. The hub contains multiple ports.
4) When a packet arrives at one port, it is copied to the other ports so that all segments of the LAN can see all packets.

Bridge
1) Bridging is the process of forwarding frames at Layer 2 of the OSI Model.
2) The Bridge is used to divide the LAN into two segment.
2) The Bridge will maintain the mac table of all hosts.

        bridge table port 2
        port 1

Port Mac / 1 a / 1 b / 2 c / 2 d

        Host 1 Host 2 Host 3 Host 4
mac address 'a' mac address 'b' mac address 'c' mac address 'd'
Ip Address Ip Address Ip Address Ip Address
192.168.1.2 192.168.1.3 192.168.1.4 192.168.1.5

3) If we want ping from HOST 1 to HOST 4.
4) The Arp packet is sent to all host the HOST 4 will reply with its mac address and the mac address of Host 1 and Host 4 is updated in bridge table
5) But Host 3 and Host 4 will have the same port.
6) So the icmp packet will be broadcast to that segment port 2 because the Host 3 and Host 4 have the same port.

Switch
1) The Every host is connected to the single port switch.
2) All host will have the different ports.
3) The switch will maintain port no and mac address of host.
        Host 1 port 1 switch Host 3 mac c

Port mac / 1 a / 2 b / 3 c

        Host 2 port 2

Router
1) The Switch will maintain the port number and mac address of every host but the router will maintain the default route along with the default it will maintain the ip address and the mac address.
        switch
host 1 mac a

Port mac / 1 a / 2 b / 3 c

    Host 2 mac 2 Router
Defaut route / ip 10.0.0.0 11.0.0.0 / ip address mac / 11.0.0.1 c

        Host 3 mac c

1) First we need add a Folder in the /fushsia/garnet/bin for example /fushsia/garnet/bin/hello
2) In the hello Folder we need to ad BUILD.gn and any C program like hello.c
3) In the BULID.gn we need to write the bin to hello.c in the hello floder and also shell , the binary name and package that we need to add.
4) In the floder /fushsia/garnet/bin/BUILD.gn make a entry of the floder name of hello
5) In the floder /fushsia/garnet/packages/prod/BUILD.gn add the path of "//garnet/bin/hello"
6) And then do the ./scripts/fx full-build in the fushsia floder
7) And then run the ./scripts/fx run in the fushsia floder
8) And then type the binary file of the hello that is present in /fushsia/out/default

Address Resolution Protocol

        1 x y 6

ee01 ee02

        2

11.11.11.10 5
 aaaa.aaaa.aaaa 22.22.22.40
gateway is 11.11.11.1 dddd.dddd.dddd
gateway is 22.22.22.1

1) ARP Table : mapping of IP address to MAC address.
2) MAC address Table : mapping of Switch ports to MAC address.
3) Routing Table : mapping of IP Network to Interfaces.

1.Host A has Data for Host D
Host A already knows Host D's IP Address
Host A creates a L3 Header
Host A needs to learn its Default gateway Mac Address
2. Host A sent a ARP Request to 11.11.11.1

3. Switch X Receives Frame
Switch X Learns Mac Address mapping on port 2
Switch X Floods
4.Host B discard from
5. Router receives ARP request
Router learns Host A's ARP mapping
6.Router generates ARP Response
7.Switch x Receive frame
Switch x learn mac address mapping on port 3
Switch x forwards frame out port 2
8.Host A receives ARP Response
Host A learns router's ARP mapping
9.Host A creates icmp L2 header and sends packet
10.Switch x receive frame
Switch x already knows mapping for port 2
Switch x forwards frame out port 3
11.Router receives packets and strip L2 header
12.Router consults Routing table
22.22.22.0/24 network exists on eth2 interface
Router needs to learn Mac Address mapping on port 4
13.Router sends an ARP Request for 22.22.22.40
14.Switch Y receice frame
Switch Y learns MAC address mapping on port 4
15.C discards
16.Host D receives ARP Request
Host D learns Router's ARP mapping
17.Host D generates ARP Response
18.Switch Y receives frame
Switch Y learns MAC address mapping on port 5
19.Router receive ARP Response
Router learns Host D's ARP mapping
20.Router creates L2 Header and send packets
Switch Y already knowns mapping for port 4
Switch Y forwards frame out port 5
21.Host D receive packets
Host D strip L2 header
Host D strip L3 header
Host D receives data frame
22.Host D reponse with Data for Host A
Host D already known Host A's IP Address
Host D creates L3 header
23.Switch consults destination Mac address.
25.Router consults routing table
11.11.11.0/24 network exists an eth1 interface
Router already knowns Host A Mac address.
26Router creates L2 header and send packets.
27.Switch x receives frame
Switch x already knowns mapping for port 3
Switch x forwards frame out port 2
28.Host A receive packets.
Host A strips L2 header
Host A strips L3 header and receive data

Router Routing Table

eth1 : 11.11.11.0/24
eth2 : 22.22.22.0/24

Bridging concept

A network bridge is a computer networking device that creates a single aggregate network from multiple communication networks or network segments. This function is called network bridging.[1] Bridging is distinct from routing. Routing allows multiple networks to communicate independently and yet remain separate, whereas bridging connects two separate networks as if they were a single network.[2] In the OSI model, bridging is performed in the data link layer (layer 2).[3] If one or more segments of the bridged network are wireless, the device is known as a wireless bridge.

https://en.wikipedia.org/wiki/Bridging_(networking)