802.11 MEDIUM CONTENTION
G. Naresh

---
 CONTENTS
- CSMA
- Distributed Coordination function
- Interframe Spaces
- Random Backoff
- Frame Transmission

---
 CSMA
- Idea: The chance of collision can be reduced if a station senses the medium before trying to use it.
- Persistent Methods
  - 1 – Persistent Method
  - Nonpersistent Method
  - p – Persistent Method
- CSMA/CD
- CSMA/CA

---
 Persistent Methods

---
 CSMA/CD

---
 CSMA/CD Flowchart

---
 CSMA/CA Flowchart

---
 Distributed Coordination Function
- The four main components of DCF:
  - Carrier sense
  - Duration/ID field
  - Interframe space
  - Random backoff timer
- Physical Carrier Sense (Clear Channel Assessment)
  - ED (Energy Detection)
  - CS (Carrier Sense)
- Virtual Carrier Sense (Network Allocation Vector)
  - Duration value set in each frame’s MAC header where other stations set their NAV to this if the sense medium is busy.

---
 Interframe Spaces
- The IFS is a quiet period that APs and stations must wait before any 802.11 frame transmission.
- The purpose of an IFS is both to provide a buffer between frames to avoid interference as well as to add control and to prioritize frame transmissions.
- The length of the IFS time is depends on previous frame type, following frame type, access category, coordination function in use & PHY type as well.
- Short Interframe Space (SIFS)
  - It is the shortest IFS, has highest level of priority.
- Reduced Interframe Space (RIFS)
  - RIFS were introduced with 802.11n to improve efficiency for transmissions to the same receiver in which a SIFS-separated response is not required, such as a transmission burst (CFB-Contention Free Burst).

---
 Contd...
- DCF Interframe Space (DIFS)
  - DIFS = SIFS + 2 x SlotTime
- Extended Interframe Space (EIFS)
  - EIFS (in DCF) = SIFS + DIFS + ACK_Tx_Time
  - EIFS 802.11b/g/n devices using DSSS = 364μS
  - EIFS 802.11g/n devices using OFDM = 160μS
  - EIFS 802.11a/n devices (5GHz) = 160μS
  - EIFS (in EDCA) = SIFS + AIFS[AC] + ACK_Tx_Time
- Arbitration Interframe Space (AIFS)
  - Shall be used by the QoS STA's.
  - AIFS[AC] = AIFSN[AC] × SlotTime + SIFSTime
- PCF Interframe Space (PIFS)
  - Used by STAs during the contention-free period (CFP) in PCF mode.
  - PIFS = SIFS + SlotTime

---
 Contd...

---
 Random backoff
- An 802.11 station may contend for the medium during a window of time known as the backoff time.
- STA shall use the Random back-off after the defer period to avoid collisions.
- Backoff Time = Random() × aSlotTime
- Random() = Pseudo-random integer select from interval 0,CW(Contention Window) .
- aSlotTime =Slot time sizes are dependent on the physical layer specifi cation (PHY) in use (DSSS, OFDM,etc. ).

---
 Contention Window
- To contend for medium access after the IFS, each station selects a backoff value called random backoff period and is selected at random by the STA from a window of possible values called a contention window (CW).
- CW = 2^k – 1.
- aCWmin ≤ CW ≤ aCWmax.
- Contention window (CW) parameter shall take an initial value of aCWmin.
- The CW shall take the next value in the series every time an unsuccessful attempt to transmit an MPDU .
- Once it reaches aCWmax, the CW shall remain at the value of aCWmax until the CW is reset.

---
 Contd...

---
 Frame Transmission

---
 Arbitration Flowchart