WLAN BASICS – Part-II
Lalith Raj P

---
Cover
- Basic Terminology
- 2.4GHz, 5GHz bands
- History IEEE 802.11a/b/g/n/ac

---
Basic Terminology
Frequency(or radio frequency)
- The rate of radio signal to send and receive communication signal
- Measured in hertz (hz), cycles per second.
- Common frequencies that are used for wifi communication are 2.4 Ghz (giga hertz per second) and 5 Ghz.

---
Basic Terminology
Bandwidth
- The upper and lower limit of the frequency used for transmitting or receiving information.
- It's also measured in hertz.
- Example: wireless network operate on 2.4 Ghz with 20Mhz bandwidth.
- Bigger bandwidth --> higher transfer rate, because more data can be transmitted on one unit of time.

---
Basic Terminology
Range
- The measurement of how far can the data/signal transmitted and received.
- In radio communication this can be from couple of meters to tens/hundreds of kilometers.
- How far the radio communication can reach is subjective to environment condition and also frequency.

---
Basic Terminology
- High frequency -> low range -> high bandwidth.
- Low frequency -> high range -> low bandwidth.

---
802.11 systems & frequency bands
A summary of the bands used by the 802.11 systems

---
2.4 GHz
2.4 GHz channels
- Total of fourteen channels defined for use by Wi-Fi 802.11 for the 2.4 GHz ISM band.
- WLAN / Wi-Fi channels are spaced 5 MHz apart
- 802.11 Wi-Fi standards specify a bandwidth of 22 MHz and channels are on a 5 MHz incremental step.

---
2.4 GHz
2.4 GHz Wi-Fi channel frequencies

---
2.4 GHz
2.4 GHz WiFi channel overlap and selection
- Channels overlap and it is possible to find a maximum of three non-overlapping channels.
- There are five combinations of available non overlapping channels

---
2.4 GHz
Three routers are all using channel 6.
The data isn't interfering
However the channel is a little contended

---
2.4 GHz
2.4 GHz Wi-Fi channel availability

---
5 GHz
- 5 GHz Wi-Fi channels fall outside the accepted ISM unlicensed band
- As a result various restrictions are placed on operation at these frequencies.

---
5 GHz
DFS = Dynamic Frequency Selection
 TPC = Transmit Power Control
 SRD = Short Range Devices 25 mW max power